## Slide 1
http://yehnan.blogspot.tw/2014/02/arduino.html

## Slide 2
#define SERIAL_BAUDRATE 115200
#define CLK_PIN 2 // 定義連接腳位
#define DT_PIN 3
#define SW_PIN 4
#define interruptA 0 // UNO腳位2是interrupt 0，其他板子請見官方網頁
volatile long count = 0;
unsigned long t = 0;
void setup() {
Serial.begin(9600);
// 當狀態下降時，代表旋轉編碼器被轉動了
attachInterrupt(interruptA, rotaryEncoderChanged, FALLING);
pinMode(CLK_PIN, INPUT_PULLUP); // 輸入模式並啟用內建上拉電阻
pinMode(DT_PIN, INPUT_PULLUP);
pinMode(SW_PIN, INPUT_PULLUP);
}
void loop() {
if(digitalRead(SW_PIN) == LOW){ // 按下開關，歸零
count = 0;
Serial.println(count);
delay(300);
}
}
void rotaryEncoderChanged(){ // when CLK_PIN is FALLING
unsigned long temp = millis();
if(temp - t < 200) // 去彈跳
return;
t = temp;
// DT_PIN的狀態代表正轉或逆轉
count += digitalRead(DT_PIN) == HIGH ? 1 : -1;
Serial.println(count);
}

## Slide 3: http://www.yd-tech.com.tw/pdf/ARDUINO/20%20Arduino%207%20Color%20Flash.pdf
/*
Blink
Turns on an LED on for two second, then off for two second, repeatedly.
This example code is in the public domain.
*/
void setup() {
// initialize the digital pin as an output.
// Pin 13 has an LED connected on most Arduino boards:
pinMode(7, OUTPUT);
}
void loop() {
digitalWrite(7, HIGH); // set the LED on
delay(10000); // wait for a second
digitalWrite(7, LOW); // set the LED off
delay(300); // wait for a second
}